XMT Controller Quality Control checklist.

# Date:  _______________          XMT S/N : _____________________

Crew Chief:______________________   Intended Job #: _________

Do you require the time series XMT?    TICK:  Yes _____   No _____

Note: Complete XMT checklist first,    before starting receiver checklist.

- Open up battery compartment and check:

- Battery in good condition &  Date on battery: _____________________

- Battery terminals all in good condition and connected.

- Measure battery voltage with Multi-meter.                      __________  volts

- Insulation tape covering terminals or areas that may short.

- Wiring harness in good condition with no damaged insulation

- External check of controller:

- Are all screws installed? Close battery compartment taking care not to pinch wiring and that battery terminals don’t short. Make sure foam is in place.

- Turn XMT on and compare measured voltage with analog meter.

- Is the controller body, lid and front panel is clean?

- Is the Hi/Low frequency table available in lid if no Freq LCD meter installed?

- Analog meter installed and in reasonable condition?

- All switches feel they work correctly and are in reasonable condition?

- Test XMT operations:

- Use scope to test calibrate jacks to see out put over a range of frequencies in 100% and 50% duty cycles.

- Plug in XMT to transmitter cable. Use LED tester from Operations Manager, test over a range of frequencies in both 100% and 50% duty cycles. Manipulate cable to test for bad connections / broken wire.

- Repeat above test with all spare XMT cables intended for job.

- Leave XMT turned on to warm up for receiver sync test.

- Sync test ok?