## Slide 2: Airborne MAGNETIC SURVEYING
Overview

## Slide 3: Want to measure: Magnetic signature from Geological formations:
Measure the distortion in the earths Magnetic field.
- Aid interpretation
- Map Structures
- Detect anomalies
Must fly a grid pattern
Height attenuation
Terrain follow

## Slide 4: Data Acquisition :
Collect 2D data:
- Fly a grid pattern
- closer line spacing=better resolution
Signal attenuation:
- Close to the magnetic source.
- Terrain follow

## Slide 5: Traditional Survey aircraft: Helicopter Systems:

## Slide 6: Traditional Survey aircraft: Fixed Wing Systems:

## Slide 7: Development of UAV magnetic survey systems:
Try to replicate Full sized aircraft with UAV:
Must Consider:
Magnetic Quality : sensitivity/ noise / interference
Survey area: Size, terrain, vegetation, access
UAV selection: performance, endurance, technology
Survey budget: $$$$$$
Constraints: Regulations, safety requirements, insurance, licensing.

## Slide 8: UAV MAGNETIC SURVEYING
First round
of UAV Mag Development

## Slide 9: Development of UAV magnetic survey systems: Early attempted Uav Mag Systems:
Fugro Airborne 1993 Georanger , 2006- Aerosonde

## Slide 10: Development of UAV magnetic survey systems: Early attempted Uav Mag Systems:
Sanders Geophysics & Columbia State University UAV: (2009 - 2014)

## Slide 11: Development of UAV magnetic survey systems: Early attempted Uav Mag Systems:
United States Geological Survey ( 2011 - 2013 )

## Slide 12: Development of UAV magnetic survey systems: Early attempted Uav Mag Systems:
China Geological Survey UAV Mag System: ( 2013 - ?

## Slide 13: Attempting to do Large area surveys Gawler-Craton survey in SA 1,800,000km

## Slide 14: Development of UAV magnetic survey systems:
Try to replicate Full sized aircraft with UAV:
Corporate attempts: Our aims:
Magnetic resolution : High sensitivity Low Resolution
Survey area: Traditional Size Small survey Area
UAV selection: Military, Custom RC technology
Survey budget: High $$$$$$ very small $
Regulations: will overcome Disregard.

## Slide 15: Major developments for the next phase of UAV Mag Development:
Low cost Autopilot – APM1.1, Ardupilot/ Pixhawk
Custom Development Data acquisition system
Long range Data Links- RFD900
Digital long range Video Links
Multi Rotor technology- Hybrid Multirotor.
Relaxation of Licensing restrictions.

## Slide 16: Development of UAV magnetic survey systems: Early attempted Uav Mag Systems:
Rada Engineering UAV Mag System: ( 2013 ) electric X8

## Slide 17: Development of UAV magnetic survey systems: Early attempted Uav Mag Systems: Custom Fixed Wing (petrol) : Rada engineering ( 2015-2017)
Wingspan 2.6 m
Endurance 1.5 hrs
Speed 70 km/h
Range: 100 km/ flight
Wind Tolerance: 20 km/h

## Slide 18: Example Flight path Flown:

## Slide 19: Flight Planning:
Customized Planning software
3D Terrain Following
Built in Survey Over fly
Flying height 30m AGL +
Line spacing 20 m +
Climb rate 20 deg
Fully Autonomous

## Slide 20: Total Magnetic Intensity Image
Line Spacing 30m
Flying Height 40m
Total Distance 120 km.

## Slide 21: 2VD Total Magnetic Intensity Image
Line Spacing 30m
Flying Height 40m
Total Distance 120 km.
Fence lines detected in 2VD. 0.5nT

## Slide 22: UAV Verses Cessna 210

## Slide 23: UAV’s do crash……

## Slide 24: The next phase- Multirotors

## Slide 25: Recent advancements- Hybrid technology

## Slide 26: Video of UAV Mag Survey: Lotta Tasmania 5 min
LIDAR Data supplied
Heavily forested
Relay drone used for communications
Towed Mag bird.

## Slide 27: Development of UAV magnetic survey systems:
UAV Hardware Development

## Slide 28: UAV Electronics:
Full Autopilot: Pixhawk
Magnetic fluxgate sensor
Data Acquisition System
LIDAR
Data telemetry to base
Autopilot datalink to base
Full data logging to USB

## Slide 29: Custom DAQ System:

## Slide 30: DATA ACQ SYSTEM:
Sample rate 50Hz
Sample interval 0.4 meters
Sensor 3 Axis high sensitivity Fluxgate
DAQ 24 Bit synchronous ADC
Magnetic Noise Sensor +/- 0.15 nT
Mag Compensation Post processed.
LIDAR 120m Range , accuracy 5cm.
RTK GPS (option) RTK system accuracy 10cm
Standard GPS Ublox M8N 12 Ch Accuracy 2m
DATA MONOTORING Real time data QC at base
Specifications @ May2016

## Slide 31: SYSTEM REMOTE DATA QC:
Data Telemetry to ground:
Magnetic data
GPS Location
Number of Satellites
Lidar Height
Battery Voltages
Engine Temperature
Electronics Temperature
Logging Status

## Slide 32: Video of UAV Mag Survey: Karratha 4 min
700 km
Stage1 photogrammetry
Stage2 UAV Mag survey.

## Slide 33: Development of UAV magnetic survey systems:
UAV Hardware Development
Magnetometers.

## Slide 34: Development of UAV magnetic survey systems: Magnetometer Selection:

## Slide 35: Development of UAV magnetic survey systems: Magnetic Sensor Comparison:

## Slide 36: Development of UAV magnetic survey systems:
MFAM Sensor
Fluxgate sensor

## Slide 37: Development of UAV magnetic survey systems:
Magnetic Noise:
The survey data is the final product, and good data quality is essential. UAV Magnetic data quality is affected by the following sources:
Sensor internal noise
Data Acquisition noise
EMI interference
Permanent magnetic interference
Induced magnetic interference
Eddie current magnetic interference
These noise sources are derived from:
Sensor and recording system.
Engine
Servos
Aircraft movement
Sensor movement
Conductive materials
Radio/ video transmitters

## Slide 38: Magnetic compensation
Must remove effects of movement
Interference of aircraft and other sources.
--Fluxgate responses due to Roll, Pitch Yaw of sensor.

## Slide 39: Magnetic compensation
Must remove effects of movement
-Profiles of maneuver noise

## Slide 40: Magnetic compensation
-Post processed Magnetic compensation.
-Typical residual noise < 0.4 nT per maneuver.

## Slide 41: Mag Compensation profile
Example Magnetic profile over irrigation pivot at 15m AGL
Raw Mag vs Compensated Mag profile.
4th Diff Noise online < +/- 0.2 nT

## Slide 42: Magnetic data Power Spectrum:
Power spectrum of Magnetic data shows no Harmonics or interference effects from UAV electronics.

## Slide 43: Video of UAV Quarry Survey 2 min
150 km Rugged terrain
Trying to define intrusive sections in Limestone
Over a working Quarry

## Slide 44: UXO Detection - DAQ

## Slide 45: Quad sensor on UAV

## Slide 46: 4 sensor Walking UXO detection system

## Slide 47: 6 sensor UXO towed cart

## Slide 48: LAOS- 4 sensor UXO Boom -light weight

## Slide 49: UXO Quad Boom coverage Map

## Slide 50: 4 Sensor results

## Slide 51: Quad sensor UXO detector on UAV

## Slide 52: Video of UAV Coal Survey2 min
1000 km Flat terrain
Trying to define intrusive Dykes
Structures in coal.

## Slide 53: UAV Coal survey Mag Data :

## Slide 54: UAV Coal Survey Data:

## Slide 55: UAV Coal Survey data

## Slide 56: THE END…
But really just the beginning of a new phase of exciting technology.